## Slide 1
FIBRINOGEN
as
FIB CONCENTRATE
or
CRYOPRECIPITATE
RETEST
RETEST
RETEST
GENERAL SURGICAL / OBSTETRIC HAEMORRHAGE ROTEM & TEG GOAL DIRECTED BLEEDING MANAGEMENT ALGORITHM (2025)
Adjust dose of blood products for patients <50kg after consulting senior clinician
Poor Platelet Contribution
Low Fibrinogen
Low Coagulation Factors or Oral anticoagulants
Hyperfibrinolysis
FIBRINOGEN
PLATELETS
FACTORS
FIBRINOLYSIS
NORMAL
YES
YES
ELP/ FFP
OR
PCC
YES
When clinically possible always complete the algorithm in a stepwise manner and check the ROTEM between steps as indicated. This reduces unnecessary transfusion especially of platelets/ELP/ Beriplex.
PROCEED WITH ALGORITHM
Tranexamic Acid
1 gram
Or 15mg/kg
Clinician discretion for Fibrinogen Concentrate
Usually for massive obstetric haemorrhage or severely low FIBTEM or CFF
YES
CLOT INSTABILITY Early diagnosis | 
EXTEM A5 <35mm | CRT A10 <47mm
Flat line FIBTEM or CRT at 5min | 
NORMAL FIBTEM A5 ≥ 12mm AND IS EXTEM A5 < 35mm? | NORMAL CFF A10 > 15mm AND IS CRT A10 < 47mm?
Or abnormal Multiplate | 
NORMAL FIBTEM A5 ≥ 12mm AND IS EXTEM CT > 85 sec? | NORMAL CFF A10 > 15mm? AND Is CKH-R > 10 minutes
Ensure core temp >36C and Fibrinogen corrected first TEG has no dedicated extrinsic test & cannot detect warfarin | 
PLATELETS
Temp >36 C, pH >7.2, iCalcium >1.1 mmol/L, Platelets >70x109/L, Hb >75 g/L
High risk of Fibrinolysis?
E.g. trauma, obstetric, major ortho Consider Tranexamic Acid 1g IV now
ROTEM & TEG
Results in 10 min
Observe
YES
NO
IS THERE CLINICALLY SIGNIFICANT BLEEDING?
Then
Repeat test 10 mins
AFTER EACH INTERVENTION
IF BLEEDING CONTINUES
CLOT INSTABILITY after 30 minutes | 
IS FIBTEM ML ≥ 10 %? | Is CRT (LY30) > 2.2%
Clot should be stable for 1 hour, not tapering away | 
FIBRINOLYSIS
Hyperfibrinolysis
YES
Consider additional tranexamic acid
IS FIBTEM A5 < 12mm? (close correlation to Clauss fibrinogen) | Is CFF A10 < 15mm? (Local validation recommended)
Including flat line at 5 minutes | 
NO
NO
NO
NO
NO
STILL BLEEDING? Consider SURGICAL PROBLEM and discuss with surgeon and blood bank/haematologist | 
Make a stronger clot? Give cryo to FIBTEM A5 > 14mm Give platelets to EXTEM A5 > 40 mm or consider Platelet Function testing Consider ELP to shorten clotting time to EXTEM CT < 80 sec | Re check temperature, pH, iCalcium, platelets and haemoglobin Consider other contributors to bleeding Platelet inhibitors (do Multiplate Platelet Function test) Consider Von Willebrands Disease, warfarin (INR), clexane etc.