## Slide 1
PAEDIATRIC ROTEM & TEG GOAL DIRECTED BLEEDING MANAGEMENT ALGORITHM (2025)
Temp >36 C, pH >7.2, iCalcium >1.1 mmol/L, Platelets >70x109/L, Hb >75 g/L
Observe
NO
NORMAL
Pool Platelets
20mLs/kg
Chronic renal dysfunction, consider
Desmopressin / DDAVP
0.3microg/kg IV
Slow infusion over 30min
IS THERE CLINICALLY SIGNIFICANT BLEEDING?
High risk of Fibrinolysis?
E.g. Trauma, craniofacial, major ortho Consider Tranexamic Acid 15mg/Kg
ROTEM
Results in 10 min
YES
Then
Repeat test 10 mins
AFTER EACH INTERVENTION
IF BLEEDING CONTINUES
RETEST
RETEST
RETEST
Poor Platelet Contribution
Low Fibrinogen
Low Coagulation Factors or Oral anticoagulants (Warfarin or DOACs)
Hyperfibrinolysis
FIBRINOGEN
PLATELETS
FACTORS
FIBRINOLYSIS
NO
NO
NO
NO
YES
YES
ELP/ FFP 20mLs/kg
OR
Beriplex
12.5 Units/kg IV
If volume overloaded
YES
PROCEED WITH ALGORITHM
Clinician discretion for Fibrinogen Concentrate
Usually single dose
Only for severely low FIBTEM <6mm or CFF <10mm
YES
CLOT INSTABILITY Early diagnosis | 
EXTEM A5 <35mm | CRT A10 <47mm
Flat line FIBTEM or CRT at 5min | 
NORMAL FIBTEM A5 ≥ 12mm AND IS EXTEM A5 < 35mm? | NORMAL CFF A10 > 15mm AND IS CRT A10 < 47mm?
NORMAL FIBTEM A5 ≥ 12mm AND IS EXTEM CT > 85 sec? | NORMAL CFF A10 > 15mm? AND Is CKH-R > 10 minutes
Ensure core temp >36C and Fibrinogen corrected first | 
Cryo or FibConc.
If FIBTEM A5< 6 or CFF A10 <10,
ensure platelets are also available
CLOT INSTABILITY after 30 minutes | 
IS FIBTEM ML ≥ 10 %? | Is CRT (LY30) > 2.2%
Clot should be stable for 1 hour, not tapering away | 
FIBRINOLYSIS
Hyperfibrinolysis
YES
Consider additional tranexamic acid
Consider APTEM if available to further investigate clot instability
E.g. Factor XIII, clot retraction
IS FIBTEM A5 < 12mm? (close correlation to Clauss fibrinogen) | Is CFF A10 < 15mm? (Local validation recommended)
Including flat line at 5 minutes Craniofacial cases, aim for higher target. | 
Tranexamic Acid
15mg/kg
Adjust subsequent dose for renal dysfunction
STILL BLEEDING? Consider SURGICAL PROBLEM and discuss with surgeon and blood bank/haematologist | 
Make a stronger clot? Give Cryo to FIBTEM A5 > 14mm Give platelets to EXTEM A5 > 40 mm or consider Platelet Function testing (in hours) Consider ELP to shorten clotting time to EXTEM CT < 80 sec | Re check temperature, pH, iCalcium, platelets and haemoglobin Consider other contributors to bleeding Platelet inhibitors (do Multiplate Platelet Function test) Consider Von Willebrand's Disease, warfarin (INR), enoxaparin etc.
When clinically possible always complete the algorithm in a stepwise manner and check the ROTEM between steps as indicated. This reduces unnecessary transfusion, especially of Platelets, ELP and Beriplex